## Slide 1: Requirements for submission, acceptance and processing of isolates for DST

## Slide 2: Learning objectives
Understand the submission process for isolates received for DST
Understand the criteria for acceptance or rejection of isolates
Understand how TB isolates are prepared for DST

## Slide 3: Content outline
Source of isolates
  Referred to DST testing laboratory from another laboratory
  Grown in DST testing laboratory
Transport to DST testing laboratory
  Biosafety
  Transport conditions
Criteria for acceptance or rejection of isolates
  Labelling, leakage
  Contamination
Preparing the isolate for DST
  Identification
  Molecular testing
  Liquid media
  Solid media

## Slide 4: Source of isolates: External
Isolates referred to DST testing laboratory from another laboratory
  Best to process sputum specimens and perform culture in laboratories near to where specimen is collected
    Contaminants may overgrow TB in sputum specimens during transport time and conditions
    Isolates more likely to survive transportation conditions
    However, biosafety requirements must be strictly followed to transport isolates
  Species identification and DST are best performed at National TB Reference Laboratory or other Quality Assured referral laboratories
    Transport time and need to re-grow isolate delays DST reporting time
  Isolates and relevant and patient information must be accurately transcribed and transported to the NTRL for DST
<number>

## Slide 5: Source of isolates: Internal
Isolates grown in DST testing laboratory
  Information on patient has already been documented when specimen received for culture
  Internal database or log books provide information on previous tests performed on this same patient
    Direct smear results on current isolate
    Results on tests performed on specimens from this patient
    Specific issues seen with previous specimens or isolates can be addressed
      Example: growth found only on either liquid or solid media
  No need for transport
    Faster turn-around time for reporting DST results
    Isolates contained within same laboratory; biosafety issues easier to address
<number>

## Slide 6: Transportation to DST testing laboratory
Isolates suspected of being TB must be transported to the DST testing laboratory
  Safely – protect transport agents from risk of infection
  Timely – ensure viable isolates for testing
  Efficiently – delivery to appropriate laboratory
  Legally – according to national and international transportation guidelines
<number>

## Slide 7: Transportation guidance
WHO Guidance on Regulations for the Transport of Infectious Substances 2009-2010
  Mycobacterium tuberculosis is classified as Infectious substance, Category A
    Capable of causing life-threatening or fatal disease
    Shipping name is UN2814 – INFECTIOUS SUBSTANCE AFFECTING HUMANS
<number>
  WHO/HSE/EPR/2008.10

## Slide 8: Basic triple packaging system
Primary receptacle
  Watertight, leak-proof
  Absorbent material
Secondary packaging
  Watertight, leak-proof
  Cushioning material
  Absorbent material
Outer packaging
  Cushioning material
  Correctly marked and labelled with appropriate shipping documents
<number>

## Slide 9: Not all countries have adopted the United Nations system
These guidelines apply whenever the UN system for the transport of infectious substances has been adopted
WHO encourages all countries to adopt this system
However, the principles described are not intended to supersede national or local requirements
<number>

## Slide 10: Basic guidance for all countries
Hand carriage of Category A infectious substances should be strictly prohibited on air carriers
Inner packages containing infectious substances should not be consolidated with unrelated types of goods
Shippers of infectious substances should ensure that packages are prepared so they arrive in good condition and present no hazard during transport
<number>

## Slide 11: Criteria for rejection of an isolate
Do not process; contact the submitter to resubmit isolate for the following reasons:
  No label on tube
  Improper or leaking container
  Isolate overgrown with contaminant
    Caution: Opening tube with mould can contaminate BSC and other specimens
Isolates may be processed if minor questions can be clarified
  Misspellings between tube and request slip
  Contact submitter to clarify questions
<number>

## Slide 12: Preparation of isolate for DST
Identification of isolate as belonging to the M. tuberculosis complex
Ensure that the TB isolate is not contaminated
Advantages of molecular or liquid medium DST
Preparation of cells for molecular testing
Preparation of cells for DST in liquid broth in the MGIT system
<number>

## Slide 13
Isolate must be identified as MTBC before performing DST!
Culture positive for AFB
Colony and Cellular morphology
Growth characteristics
Biochemical tests
Antigen detection
Line-probe assay
DNA probe
Conventional testing
Molecular testing
Non-tuberculous mycobacteria can be resistant to anti-TB drugs, and testing can result in inappropriate patient therapy

## Slide 14: Growth of contaminants on solid media
<number>
LJ medium contains bacteriostatic agent
  Malachite green inhibits most environmental and normal flora
  Important to remove liquid in bottom of LJ before inoculation. Loosen cap for 1st week of incubation
    Limited exposure to malachite green, so contaminants may eventually grow in this liquid
Contaminated LJ medium
  If contamination is slight, attempt to isolate TB colonies; transfer to new LJ
  If totally contaminated, request a new specimen
Notes: <number>

## Slide 15: Growth of contaminants in MGIT tubes
<number>
Contaminated MGIT tubes usually become positive very early:
  24 – 48 hours
  Rapid growers such as M. avium-intracellulare complex (MAC) may be positive in 3–4 days
Visual observation:
  Homogeneous turbidity
Non-acid-fast bacteria may be seen in AFB smear of MGIT tube
  With or without AFB
Subculture to blood agar plate
  Growth in 24–48 hours
Notes: <number>

## Slide 16: DST performed using solid media
Possible problems with egg-based media (LJ)
  Potency of drugs may be diminished during inspissation
  Components of the eggs (phospholipids, proteins) affect some drugs
Middlebrook 7H10 agar with OADC
  OADC is expensive
  Lot-to-lot variations in quality have been reported
DST on solid media requires 3 to 4 weeks of incubation
<number>

## Slide 17: Gold standard for DST
Agar proportion method using Middlebrook 7H10 with quality assured OADC
  Considered the standard method for TB DST in the USA and many European countries
Most first- and second-line drugs can be accurately tested for susceptibility or resistance using this method
However, because of the long turn-around time, the method is more appropriate for surveillance than for individual patient treatment
<number>

## Slide 18: Advantages of molecular or liquid medium DST
Molecular methods
  Can be performed within 1–2 days
  Identification of TB is included in LPA
  Detection of MDR TB is quite reliable
  Accurate results may be obtained even with mixed culture
  However, not all drugs are currently available
Liquid medium DST using the MGIT system
  Results ready within 7–10 days
  Currently validated for all 1st-line drugs including PZA and some 2nd-line drugs
<number>

## Slide 19: Preparation of cells for molecular testing
Prepare suspension of cells in sterile water
  Bacteria grown on solid medium (LJ)
    Remove cells from slant with loop
    Prepare suspension in 300 µl of sterile water
  Bacteria grown in liquid medium (MGIT broth)
    Transfer 1 ml portion of the suspension to a micro-centrifuge tube
    Centrifuge for 15 min and resuspend pellet in 300 µl of sterile water
<number>

## Slide 20: DNA extraction for molecular testing
Incubate bacterial cells for 20 min in a 95 oC water bath (kills cells)
Incubate bacterial cells for 15 min in an ultrasonic water bath (optional for isolates)
Centrifuge and use approximately 5 µl of the supernatant for PCR
<number>

## Slide 21: Preparation of isolates for MGIT DST
Isolates can be grown either on solid or liquid media prior to being tested in the MGIT DST
  Need healthy cells in logarithmic phase of growth
  Need fairly light inoculum so that drug concentrations are not overwhelmed
Growth should be AFB-positive and identified as a pure culture of the MTB complex before further testing
<number>

## Slide 22: Inoculum from the MGIT tube
Adhering to the following recommended timeframe is important for accurate results
  The day a MGIT tube is positive by the instrument is considered Day 0.
  The tube should be kept incubated for at least one more day (Day 1) before DST
    May be incubated in a separate incubator at 37 ºC + 1 ºC
  A positive tube may be used for DST up to (Day 5)
    A tube that has been positive for more than 5 days should be subcultured into a fresh MGIT tube and incubated until it is positive; use this tube from 1 to 5 days of instrument positivity as described above
  If growth in a tube is on Day 1 or Day 2, vortex to break clumps, let big clumps settle for 10 minutes and use the supernatant undiluted for inoculation of the drug set.
  If growth is on Day 3, 4 or 5, vortex to break clumps, let big clumps settle for 10 minutes and then dilute 1.0 ml of the positive broth with 4.0 ml of sterile saline. This will be a 1:5 dilution. Use this well-mixed diluted culture for inoculation.
<number>

## Slide 23: Inoculum from growth on solid medium
Use growth on solid medium within 15 days of appearance of positive growth
Transfer a large amount of growth into a tube with broth or saline and glass beads; vortex the tube for 1–2 minutes to break the clumps – the turbidity should be > McFarland #1.0
Let the suspension stand undisturbed for 20 minutes, then transfer the supernatant into another sterile tube
Let this tube stand undisturbed for another 15 minutes then transfer the supernatant into another sterile tube – the turbidity should > McFarland #0.5
Adjust the turbidity of this suspension down to McFarland #0.5 by adding sterile saline; do not make it below this standard
Dilute the above suspension 1:5 by adding 1.0 ml of the suspension to 4.0 ml of sterile saline; mix well and use it as the inoculum for drug susceptibility testing
<number>

## Slide 24: Summary: Isolates for DST
Isolates can either be grown in the DST testing laboratory or referred from another laboratory
Transport of isolates to the DST testing laboratory must be safe, timely, efficient and legal
Isolates should not be tested if they are unlabelled, leaked, or overgrown with mould
DST using molecular or MGIT system methods have much shorter turn-around times than DST using solid media
For phenotypic DST, growth should be AFB-positive, and identified as a pure culture of the MTB complex
<number>

## Slide 25: Acknowledgement
<number>