## Slide 1: Worksheets and labelling for BACTEC™ MGIT™ 960 drug susceptibility testing
Content adapted from standardized Becton Dickinson, WHO, GLI, CDC and NHLS Training Materials for use by the African Centre for Integrated Laboratory Training, 2011
Notes: <number>

## Slide 2: Training outline
<number>
DST worksheet
  Determining the age of a MGIT seed tube
  Determining what dilutions need to be prepared
Barcode and Dot labels
Notes: <number>

## Slide 3: TB MGIT DST log sheet
<number>

## Slide 4: TB MGIT DST log sheet
<number>
Enter the date inoculated and initials

## Slide 5: TB MGIT DST log sheet
<number>
29/03/2011
List laboratory serial numbers for DST

## Slide 6: Using the TB MGIT DST log sheet
<number>
29/03/201
2011482012
2011482014
Additional information – TB register no., referred from another laboratory, etc.

## Slide 7: Using the TB MGIT DST log sheet
<number>
29/03/201
2011482012
2011482014
56-241-2
52-483-5
Indicate what type of media the seed inoculum is growing on, usually MGIT or LJ

## Slide 8: Using the TB MGIT DST log sheet
<number>
29/03/2011
2011482012
2011482014
56-241-2
52-483-5
MGIT
MGIT
MGIT
Tick test(s) to be inoculated

## Slide 9: Using the TB MGIT DST log sheet
<number>
29/03/201
2011482012
2011482014
56-241-2
52-483-5
MGIT
MGIT
MGIT
X
X
X
X
X
Record age of MGIT seed tubes. Use the Unloaded Positives Report to determine the age of each MGIT and write it in the cell
***Remember that the day the MGIT instrument indicated that it is positive is day 0

## Slide 10: Unloaded positives report
<number>
Age in days

## Slide 11: Using the TB MGIT DST log sheet
<number>
29/03/201
2011482012
2011482014
56-241-2
52-483-5
MGIT
MGIT
MGIT
X
X
X
X
X
3
3
Will a 1:5 dilution need to be made??
If the seed tube is 1 - 2 days old, no dilution is needed
If seed tube is 3 - 5 days old, 1:5 dilution is needed

## Slide 12: Using the TB MGIT DST log sheet
<number>
29/03/201
2011482012
2011482014
56-241-2
52-483-5
MGIT
MGIT
MGIT
X
X
X
X
X
3
3
Y
Y
If a PZA drug set is inoculated, a 1:10 dilution is needed to inoculate the PZA growth control
Look here to see if PZA is needed

## Slide 13: Using the TB MGIT DST log sheet
<number>
29/03/201
2011482012
2011482014
56-241-2
52-483-5
MGIT
MGIT
MGIT
X
X
X
X
X
3
3
Y
Y
Y
Y
N

## Slide 14: DST set-up and labelling

## Slide 15: Use the checklist to gather supplies
MGIT DST Checklist |  | 
l |  | 
Labelling and set-up |  | Tick
1 | Worksheets | 
2 | Barcode labels | 
3 | Coloured dot labels | 
4 | MGIT DST carriers (5 and 2 tube) | 
5 | MGIT DST Transport racks | 
6 | Permanent marker fine point | 
7 | Saline blanks (9.9 ml, 4.5 ml and 4.0 ml) | 
8 | Blood agar plates | 
9 | 7H10 plates | 
10 | MGIT tubes | 
11 | PZA Tubes | 
<number>

## Slide 16: Definitions for set-up and labelling
<number>
DST or AST Transport Rack
DST or AST Carrier
Barcode label
Dot labels

## Slide 17: DST set-up
Use the DST log sheet to determine which sets (SIRE and/or PZA) to inoculate
Place the needed DST carriers on the transport rack
Place MGIT and PZA tubes in the carriers
  PZA testing requires the use of PZA medium
<number>

## Slide 18: Labelling
Each DST set is given 1 barcode label
  This label is placed vertically on the Growth Control (GC) tube
<number>

## Slide 19: Dot decoder
<number>

## Slide 20: Dot labels
Write the specimen ID number on each growth control dot label (yellow)
Write the first initial of each drug and set serial number on the appropriate coloured dot
  The set serial number is found in the far left column of the MTB MGIT DST worksheet
Apply dots to the tops of the MGIT tubes
<number>

## Slide 21: Saline dilution tubes
All SIRE DST sets will need a 9.9 ml saline blank (1:100 dilution)
All PZA DST sets will need a 4.5 ml saline blank (1:10 dilution)
Only seed tubes that are 3–5 days old will need a 4.0 saline blank (1:5 dilution) (check worksheet)
<number>

## Slide 22: Saline dilution tubes
Label each saline blank or dilution tube with the Specimen ID number and the dilution
Place in a rack as shown in the diagram
Leave the front row empty for the seed tubes
<number>
The 4.0 ml saline blank is used to prepare the 1:5 dilution needed if the MGIT seed tube is 3-5 days old.
****This tube is not needed if the MGIT seed tube is 1-2 days old
The 4.5 ml saline blank is needed to prepare the 1:10 dilution that will be used to inoculate the PZA growth control (GC) tube
The 9.9 ml saline blank is needed to prepare the 1:100 dilution that will be used to inoculate the SIRE growth control (GC) tube

## Slide 23: Summary
<number>
Use the information on the Unloaded Positives Report to fill out the DST worksheet
Place MGIT/PZA tubes in carriers in the transport rack
Stick the appropriate barcode label on each growth control tube
Label each drug tube and GC tube with the correct dot label
Label and place the necessary saline blanks in a rack; refer to the DST worksheet to determine which dilutions are necessary

## Slide 24: Acknowledgement
<number>