## Slide 1: Second-line drug preparation for MGIT 960 DST
Notes: <number>

## Slide 2: General drug preparation considerations
<number>
Drugs may be prepared in stock solutions that are stored frozen and later thawed and diluted for use; solvents are not always distilled H2O
Drug solutions must be sterile-filtered prior to addition to MGIT tubes, either the stock solutions or diluted working solutions
Filter membranes must be compatible with final drug solvent
Notes: <number>

## Slide 3: Filter membrane guide (1)
<number>
Notes: <number>

## Slide 4: Filter Membrane Guide (2)
<number>
Drugs prepared in a non-aqueous solvent but diluted in distilled H2O may be filtered through a membrane compatible with water but not the initial solvent
All filter membranes in the above tables are compatible with water
Notes: <number>

## Slide 5: Potency/purity
<number>
Drugs are purchased as powders that vary in activity from lot to lot
The activity of a specific drug lot is listed as potency or purity on the Certificate of Analysis (C of A) supplied by the vendor
Drugs at or near 100% potency may be weighed out without adjustment (it can be assumed that 10 mg powder = 10 mg active drug)
Notes: <number>

## Slide 6: Potency variability
Potencies may not be close to 100% because:
  There are other materials in the powder, such as impurities, preservatives or solubilizers
  Potency standards may be decades old and drug manufacturing processes have changed since the standards were established

## Slide 7: Potency adjustment
If the potency of a given drug is 74.5% (or 0.745 µg/ml), how would you prepare 10 ml of a 1% solution?
  0.01 grams × 10 ml = 0.1 gram
  Potency adjustment: 0.1 grams/0.745 = 0.134 grams powder
  Weigh out 0.134 grams powder and dissolve in 10 ml for a 1% potency-adjusted solution

## Slide 8: Today’s second-line drug preparations
<number>
Critical concentrations for MGIT960 second-line anti-TB drugs are from WHO guidelines
Formulations are from NHLS Diagnostic Media Products (DMP)
Ethionamide (ETH): Sigma E6005, critical concentration = 5 µg/ml
Ofloxacin (OFX): Sigma O8757, critical concentration = 2 µg/ml
Notes: <number>

## Slide 9
<number>
Notes: <number>

## Slide 10: Ofloxacin preparation: DMP formulation
<number>
OFX critical concentration = 2 µg/ml
Lot 040M1313V: 100% purity (no potency-adjustment necessary)
Solvent & diluent: sterile distilled H2O
MGIT DST tubes contain 8.4 ml total
8.4 ml × 2 µg/ml = 16.8 µg per MGIT tube
0.1 ml ×168 µg/ml added per MGIT tube
5.95 ml sterile dH2O × 168 µg/ml = 1000 µg
Notes: <number>

## Slide 11: Ofloxacin preparation: DMP formulation
<number>
Filter membrane available: cellulose acetate, 0.2 or 0.22 µm
Attach syringe filter to a 10 ml syringe; filter-sterilize into sterile cryovials and freeze immediately
Thaw just prior to use and do not re-freeze; discard any leftover solution
Notes: <number>

## Slide 12: Acknowledgement
<number>